## Slide 1: CEIR Product/Platform - Training Manual

## Slide 2
Product/Platform Overview
  About CEIR
  Use Case
  Stakeholder Overview
  Feature Overview
  Deployment Architecture
  Integration Touch Points

## Slide 3: Product Overview
Key objective and functionality of CEIR is to block (or maintain black listing for blocking and grey listing for monitoring) the devices in multi operator’s environment homogeneously without any preference or selection for multiple reasons or objectives from using the network services like voice, SMS, GSM data(not Wi-Fi data).
CEIR systems are also used for synchronizing the multiple EIRs from multiple network Operators in a country.
The only basis of blocking the device is IMEI / ESN / MEID of the device
There are scenarios where a local EIR in Operator’s environment or Central EIR at CEIR authority can take precedence to execute or trigger the user data collection and barring action. It is completely a case depends on country, regulation and law.

## Slide 4: Blocking of Device ??? Why it is required to be done

## Slide 5: Use Case
Active GSM Devices OR imported GSM devices personally by end customer which have not paid taxes or have pending TAX liability
  Include both new handset and second hand handset
  In stock devices with retailer / distributors
  Device bought but not in use (in-active) ( in used only in specific conditions)
Lost or Stolen devices locally and internationally
Substandard Devices (IMEI) which are not following GSMA standard or failed IMEI validation algorithm and may cause service, quality or health related issues
/Null/All 0’s IMEI devices which possibly also impact the network, end user of device or environment and create issue with LI (Lawful interception) based on IMEI as such devices cannot be tracked
Locked GSM devices for a country or network for foreign country and unlocked illegally in local market
Active devices registered in the name of illegal immigrants ex. expired visa or no visa (Security)

## Slide 6: Key Issue Addressed
Counterfeit Phones
Manufacturer loss $
No warrantee
Safety Issues
Poor Performance
Illegal Import
Government Taxation
Loss $
Un-level playing field
For legitimate device
providers
Phones Theft
Consumer loss $
Personal Injury
Buying stolen good
Insurance claims
Insurance fraud
Subscription Fraud
Operator Loss $

## Slide 7: Blocking of Devices ? All ? Any Exception

## Slide 8: Exception List
VVIP List
Roamer using local network SIM card with grace period / active visa period
Guest roamers with foreign SIM
Registered Devices under grace period
Devices that on WiFi usage and does not use cellular network

## Slide 9: IMEI - Definition
IMEI Stands for International Mobile Equipment Identity
Every mobile device that connects to cellular network has unique IMEI
This include cell phones, smartphones, cellular enabled tablets, smart watches, and other devices that support cellular data
IMEI numbers are produced by manufacturers
  GSMA stands for an international organization that oversees network operators.
IMEI is 15 digit long number
  14 digit unique number
    8 digit TAC number – allocated by GSMA
    6 digit serial number – allocated by manufacturers
      Maximum 1 million devices
      Each brand/model will have same TAC
    1 digit Check Digit
      Luhn’s Algorithm to validate IMEI number
  IMEISV
    14 digit IMEI number
    2 digit Software Version
    Will change after software update
Dial *#06# to know your IMEI

## Slide 10: IMEI - Categorization
10
IMEI
White
List
Black
List
Whitelisted to be allowed to be used in country and access network
Black list NOT to be allowed to be used in country
Valid IMEI:
TAC Approved
Taxes Paid
VIP List
In-Valid IMEI:
Non Tax Paid
Stolen Device
Not allowed to be used due to regulation in country
Zero or NULL IMEI
International Mobile Equipment Identity
Grey List
Grey Listed to be allowed to be used in country for specific duration **

## Slide 11: Typical Architecture
Operator Network
Operator Network
Operator Network
EIR
EIR
EIR
CEIR
Secured Public Access Network
DB
DB
DB
DB
Operator Specific
Data
All Country Operator Specific
Data
DB
All Operator WorldWide Specific
Data
Once all DB are synced, then the all DB are same and have the same copy

## Slide 12: Device Management Control System
DMC (Regulator)
DB
Customs
Industry/
Importers
Illegal Market
Rules
Market / End User
Set of Guidelines/Process

## Slide 13: Stakeholder Overview

## Slide 14: Stakeholder Overview - Contd

## Slide 15: Stakeholder - Feature Overview

## Slide 16: Stakeholder - Feature Overview

## Slide 17: Platform – Architecture
CEIR (Hosted in DMC IT Network)
DB
Customs
Industry/
Importers
Manufacturer
Retailer/Distributor
End User
(Local/Expat/Foreigner)
DB
TAC
Allocation Process
Device Physical Flow
HTTPS
HTTPs
Set of GSMA
Process
Secured API
Web Client
Secure
HTTP
Interface
Device Logical Flow
Set of
Operator Process
Set of Process(One set of each User Type)
…
Operator ‘s Network
DB
DB
FTP/HTTPs
SMS Interface
SMS/Payment Gateway Network
HTTP
Law Agency/Immigration/TRC/Operator
HTTPs/FTP
Interface

## Slide 18: Platform – Features
Product Features
Consignment
Stock
Grievance
User Management
Stolen and
Recovery
Block and Unblock
Grey List
Black
List
Register Device
Register
User
Anonymous
Stock
Upload
Check IMEI
Policy
And Rules
GSMA
Integration
SMS Integration
ETL Integration
Audit
Management
SLA
Management
Alert Management
Reporting
Visa Update
Configuration
Management
Payment
Integration
Customer
Care
Interface

## Slide 19: Platform – Integration
DMC IT Network
CEIR System
OTA Server
Collector
Server
Mediation
Server
PRTG Server
Email Server
SMS Server
Customer Care
SMTP
HTTPs
Agent-based Interface
Operator IT Network
Users*
Public Network
HTTPS
HTTPS
GSMA
MSC /SGSN
Server
Users*: Importers, Customs, Police, Dealer, NID Register, Immigration Department, TRC, Company Registration Department
HTTPS
FTP
HTTPS
Payment GW
HTTP

## Slide 20: Platform – Integration
ETL for Operator CDR via FTP
Bulk SMS Aggregator for sending SMS over HTTP
Email Server for sending e-mails over SMTP
PRTG for alerts over ssh based interface
GSMA over HTTP(s) for global blacklist/TAC details
Payment Gateway for Device Activation Fee over HTTPs

## Slide 21: Logical Databases – Stakeholder Mapping

## Slide 22: Deployment Architecture

## Slide 23: Redundancy Architecture
Heart Beat Layer
Single IP between two servers called virtual IP
Each server has physical IP
Virtual IP is managed by Heart beat layer
Active / Standby Configuration
Virtual IP is on the active server

## Slide 24: System Configuration
Two Phases
  Grace (Phase I)
  Post Grace (Phase II)
System Policy/Rules will be applied in post grace period.
Grace period is for building the system database
Each Policy will have a order and priority. If any policy execution fail, then the action would happen as per defined logic
Actions
  System Regularized – The system regularize will be done in grace period, wherein all the devices will be allowed to operate in the network irrespective of policy violation
  User Regularised – The User regularize is in post grace period, where the blocking/unblocking of device in network will depend on the user action against the policy violation notification
  Blocked – The device usage has been restricted from use in the network
  Allowed – The device usage is permitted for use in the network