## Slide 1: CEIR GSMA - Training Manual

## Slide 2
Agenda
  GSMA Definition and Overview
  Assumptions
  Features
    TAC
    Global Black List
  System Flow
  Impact

## Slide 3: GSMA - Definition
GSM Association (GSMA) represents the interests of mobile operator worldwide uniting more than 750 operators with almost 400 companies in the broader mobile ecosystem including handset and device makers, software companies, equipment providers and internet companies.
As the body authorized by 3GPP to allocate TAC (Type Allocation Code) for all GSM mobile devices identities globally, the GSMA is the source of authoritative and complete IMEI data.
GSMA provide two key services:
TAC Allocation
Black List Database
GSMA body is only body which has the IMEI and TAC database and hence it becomes very critical to integrate with GSMA for all the device TAC to be validated in order for effective regulation.

## Slide 4: Overview

## Slide 5: TAC - Overview
Type Allocation Code (TAC) is first 8 digits of the IMEI or MEID
All manufacturer / brand owner should get TAC allocated from GSMA before manufacturing the device
A TAC represents the complete device profile. This includes
  Brand Name
  Model Name
  Device Type
  OS Type
One TAC represents 1 million devices. So if company want to manufacturer 2 million Apple 7 devices, the company should request 2 TAC from GSMA

## Slide 6: Global Black List - Overview
In a growing number of country, operator allow subscriber to to report a mobile phone or device as lost or stolen using device’s unique IMEI.
The operator can then block the device in their mobile network. This is called IMEI blacklisting
This blacklisted devices are provided to GSMA by mobile operators
GSMA provide a API to check if device (IMEI) is blacklisted or not.

## Slide 7: API - Overview
TAC API
  Call this API when a new TAC is found in the system
  Input: TAC
  Output: Status: Approved/Not Approved. If approved then also returns device profile. Key parameter include model name, brand name, OS Type, Device Type
Black List API
  Call this API to find if IMEI is blacklisted or not
  Input: IMEI
  Output: Device Status (blacklist/Ok), Date of Blacklisting

## Slide 8: API – Implementation
To avoid over usage of API, the following logic is implemented
Database | Description
Local TAC DB (LTAC) | When a new TAC is found in the system, TAC API is called. If TAC is found to be valid, then entry is made in this database. This entry is permanent
Local Invalid TAC DB (LiTAC) | When a new TAC is found in the system, TAC API is called. If TAC is found to be invalid, then entry is made in this database. This entry is temporary and is deleted after configurable period of time. This database is mutually exclusive from local TAC DB
Global Black List DB (GBS) | When a new IMEI need to be checked for blacklisting, Blacklist API is called. If device is found to be blacklisted, then entry is made in this database. This entry is temporary and is deleted after configurable period of time.

## Slide 9: TAC API – Calling Sequence
Check local TAC DB
Check local invalid TAC DB
Check TAC
Yes
No
Yes
No
Return TAC details
Return TAC details
Call TAC API
Wait for Response
Update TAC DB / invalid TAC DB
Key Points
  Invalid DB is cleaned after configurable period of time. Once cleaned and new TAC request is found in the system, TAC API is called.
  In case the response is not received within configurable period of time, the system will keep retrying till the response is received.

## Slide 10: Black List API – Calling Sequence
Check local Black list DB
Check IMEI
Yes
No
Return IMEI details
Call Blacklist API
Wait for Response
Update Global Black list DB if required
Key Points
  Global Black list DB is cleaned after configurable period of time. Once cleaned and new IMEI need to be checked, Blacklist API is called.
  In case the response is not received within configurable period of time, the system will keep retrying till the response is received.

## Slide 11: GSMA – CEIR Interface / Protocol
3.4 Integration Approach
GSMA
HTTPS Public Network HTTPS
Diagram: Expected Integration of GSMA with CEIR system on HTTPs interface

## Slide 12: Impact
As part of the work flow, two key critical DB is created, which is used for policy implementation
TAC Database
  To check if the IMEI is valid. If IMEI contain a invalid TAC, then IMEI is considered as invalid
  Device Reporting (Type of devices in network)
Black List Database
  To ensure legal devices are used in the country
  If device is blacklisted, it is considered as illegal.

## Slide 13: Queries

## Slide 14: Thank You